## Slide 1
Optimus Mexico
PV + BESS revenue optimization for the Mexican electricity market
System overview & flow | June 2026 | Goldbeck Solar

## Slide 2
What is Optimus Mexico?
Purpose: estimate how much money a solar + battery project would make at any node of the Mexican electricity market — and whether a behind-the-meter battery pays off for an industrial CFE customer.
Two analysis tracks in one tool:
  Wholesale (MEM): CENACE hourly PML prices + PV profile → optimized BESS dispatch → revenues from energy arbitrage, PPAs and the capacity market.
  Behind-the-Meter (CFE): 15-minute load data → CFE bill reconstruction (GDMTH) → peak-shaving / TOU dispatch → investor decision with GO / REVISE / NO-GO.
Deliverables: interactive web app, Excel / Word / PDF / PowerPoint reports, investor-grade summaries, full pytest-verified calculation engine (42 tests).
Built to be integrated into Optimus AI after testing.

## Slide 3
System flow — wholesale market track
CENACE node catalog
~3,000 NodosP enriched with zona, tipo, gerencia, estado
Node Resolver
pick nodes from dropdown or extract from PML reports
Market & PV data
8,760 h PML prices + PV production profile
BESS dispatch
price-rank heuristic or daily linear optimization
PPA / Capacity
contract structures + 100 critical hours credit
Reports
Excel, Word, PDF, PowerPoint + investor report

## Slide 4
The app — horizontal navigation, four pages
How it works — purpose, pipeline diagram, data inventory with live found/missing status.
0. Node Resolver — searchable catalog dropdown with filters.
1. Dispatch + PPA + Capacity — wholesale revenue analysis.
2. Behind-the-Meter (CFE) — industrial bill-savings and investor case.
Launch: double-click run_app.bat (creates venv and installs dependencies automatically).

## Slide 5
Module 0 — Node Resolver
Every project starts at a node: the price point where energy is settled.
Enriched CENACE catalog: 2,999 nodes with zona de carga, tipo (generación/carga), gerencia regional, estado and municipio.
Pick nodes from a searchable dropdown (filter by zona, estado, tipo) — or extract node keys from a CENACE PML report (PDF/CSV/XLSX).
Output: resolution workbook with full node context, ready for the dispatch module or the PML scraper.

## Slide 6
Module 1 — Dispatch, PPA & Capacity (wholesale)
Merges 8,760 h of nodal PML prices with the PV production profile.
Battery dispatch engines:
  price_rank — transparent daily heuristic (charge cheap, discharge expensive)
  lp — daily linear program with SOC carry-over, efficiency and cycle limits
Duration sweep 2-8 h finds the most profitable battery size.
PPA structures: pro-rata, baseload block, solar-only — vs merchant.
Capacity market: 100 critical hours → accredited MW → MXN/year.

## Slide 7
Module 1 — Revenue results & reports
Interactive charts: average-day dispatch profile, single-day detail (flows + SOC + price), annual revenue by stream, monthly stacked revenue.
Sample-data result: MXN 238M total revenue (PPA 104M + Capacity 68M + Merchant 61M).
One click exports: Excel workbook, Word, PDF, PowerPoint — plus the investor report PDF with executive summary and disclaimer.

## Slide 8
Module 2 — Behind-the-Meter (CFE) — how it flows
15-minute load + PV data
customer meter data; sample plant included
CFE tariff calendar
GDMTH base / intermedia / punta, seasons, holidays
Baseline bill reconstruction
energy by period + capacity & distribution demand (CNE 2026 formulas)
BESS / PV+BESS dispatch
no-export: peak shaving cap + TOU shifting + PV self-consumption
Optimized bill + savings
savings attributed by tariff component
Investor layer
financing, haircuts, NPV/IRR over BESS life → GO / REVISE / NO-GO

## Slide 9
Module 2 — Daily dispatch & bill savings
The battery keeps grid import under a monthly cap (found by binary search) and shifts punta-period energy to cheap base hours.
PV serves load first; surplus charges the battery; nothing is exported.
Sample plant (956 kW peak, 500 kWp PV, 300 kW / 600 kWh BESS):
  CFE bill before: MXN 11.67M/yr → after: MXN 8.68M/yr
  Annual savings: MXN 2.99M | peak shaved 956 → 845 kW | zero export

## Slide 10
Module 2 — Investor decision layer
Converts the technical model into an investment answer for an owner-manager.
Explicit costs: CAPEX (USD/kWh × FX), OPEX %/yr, insurance %/yr, financing (cash / lease / loan) and a configurable BESS life (default 20 years).
Conservative haircuts: savings confidence 90%, availability 95%, collection 95%; downside case stresses tariff spread and load.
Outputs: net monthly AND annual benefit (base/downside/upside), simple payback, NPV over BESS life, unlevered project IRR, red flags.
Deterministic gate: GO / REVISE / NO-GO — reproducible from saved metrics.
Sample result: payback 1.3 y, NPV(20y) MXN 15.6M, IRR 74.6% → GO.

## Slide 11
Technology, quality & next steps
Stack: Python, Streamlit, pandas, scipy (HiGHS LP), Altair charts, openpyxl / python-docx / reportlab / python-pptx for reports.
Agent architecture: each capability is an isolated, testable module — ready to plug into Optimus AI.
Quality: 42 automated tests (tariff calendar, bill formulas, dispatch SOC and no-export constraints, financing math, recommendation gates).
Data: official CENACE node catalog (auto-download + enrich), CNE 2026 starter tariffs, synthetic sample profiles for instant demos.
Next: CENACE PML live scraping hardening, CFE/CNE tariff scrapers, PDF bill parser, DIST/DIT tariffs, multi-year PPA cash flows, Optimus AI integration.